## Slide 1: Bumpers 101
FIRST Team 67
The HOT Team

## Slide 2: Design
Step One: Design your robot
  Finalize Dimensions
  Watch out for holes in frame that need to remain uncovered

## Slide 3: Cut the Wood
Using outside dimensions for your robot’s frame, cut your wood of choice.
  Plywood is a good option, plenty strong enough for this
  Pieces should form a layer outside your robot’s frame
This year we recycled the wood from previous year’s bumpers to make a rookie team’s

## Slide 4: Drill, Secure and Reinforce Bumpers
Drill holes for wood screws to form simple butt joints.

## Slide 5: Cut angle
Use metal angle pieces on the frame side to reinforce your joints, using screws running perpendicular to the angle to secure them.

## Slide 6: Finishing
Encircle bumpers in pool noodle, wrap with plastic wrap, and seal plastic wrap with a quick once over with a heat gun.

## Slide 7: Team #’s and The Cloth Wrap
Cut cloth to wrap around the bumpers. Cut numbers for your team and glue or iron them in place. Staple cloth in place.